## Slide 1: Analysis of US Power Plant Outages from an Equipment Breakdown Insurance Perspective
Stephen Patti
Springboard Data Science Capstone Project
April 2018 – September 2018

## Slide 2: Data Sources
This study will examine the causes of US power plant outages based on the following data from the North American Electrical Reliability Corporation (NERC) Generating Availability Data System (GADS).
CC_GT_2011_2017.csv - Combined Cycle Power Plants
GT_Jet_Engine_2013_2016.csv - Simple Cycle Power Plants
Fossil_steam_2013_2017.csv - Fossil Fuel Fired Boiler Steam Power Plants
Since all equipment found at Simple Cycle Power Plants is found at the others, and my preliminary analysis did not show differences with respect to outage duration (Time_To_Repair), I did not use this data set.

## Slide 3: Objectives
As alluded to in the title, I am looking at this from the perspective of my role in commercial property and equipment insurance. I started with the following questions.
  What equipment or equipment systems are most responsible for unplanned outages?
  We have thresholds for larger losses (outages): PML – Probable Maximal Loss, MFL – Maximum Foreseeable Loss. What equipment is most closely related to these failures?
  Will this data, as used in the statistical modeling and analysis methods I’m about to study, provide any predictive value?
  How else might this analysis help my company and out customers?

## Slide 4: Preliminary Data Wrangling and Cleaning
My initial data wrangling steps included the following.
Cleaned (mutate) column/variable names, removing periods and spaces and replacing with underscores
Combined separate date and time fields to one POSIX.ct formatted field for start and end of outage
Used Select to create data frames with desired fields
c_cycle_worka <- c_cycle_work %>%
select(Util_Unit, start_dt, Type, Cause_Code, end_dt,
Time_To_Repair, TBF_Period_Hrs, IA_PH,
TBF_Service_Hrs, IA_SH, X_Derate)
Filtered the data to exclude planned, maintenance, or reserve outages, i.e. include only force outages or outages due to failures and accidents.
type_filter <- c("D1", "D2", "D3", "D4", "SF", "U1", "U2", "U3")
ff_steam_df <- ff_steam_df %>%
filter(ff_steam_df$Type %in% type_filter)